## Slide 1: Smart Sin relay switch
Serhii Fediakov
serhii.fediakov@gmail.com

## Slide 2: Idea description
If relay is connected to the capacitive load, it has huge inrush currents during the switching which decreases relay’s life time. To extend relay switch quantity, switching current should be minimized.
It could be achieved by zero-cross relay connection. But relay’s switching time is to long, near 5msec which is too much for 50/60Hz network. In addition, every relay has unique switching time which is to huge to be constant. So it need to be actualized after every switch to realize connection as close as it possible near to zero cross.
On the next slide would be described idea how such alghorithm could be realized. It was particulary implemented in Smart_Sin.ino

## Slide 3
Switch command Received
Measure sine period time
Wait until zero-cross
Wait (sine period/2-switching time)
Increase voltage to 21V
Wait until current would not be 0
|current| trend increasing
Switch relay
Record current measurement
Increase switching time variable
Decrease switching time variable
1st recorded non 0 current value is close to 0?
Decrease voltage to 12V
Yes
No
No
Yes
It decrease
switching dispersion
END